## Slide 1: LVOOP Workshop
Introduction in Object-Oriented Programming with the NI - Actor Framework
Dr. Holger Brand, GSI

## Slide 2: Agenda
Prerequisites
Motivation: Active objects
LVOOP
  Pros & Cond
  Application
  NI Actor Framework
  Example: UPN-Calculator
References

## Slide 3: Prerequisites
LabVIEW Basics 1 & 2
  Project Explorer
  Libraries
  Dataflow concept
Is knowledge about object oriented programming necessary?
  No!
  LabVIEW-Classes enables a developer to define his own data types, that provide much more abilities than (strict) type-definitions.
  Experience with conventional OO programming languages, e.g. C++ or Java, is maybe confusing.

## Slide 4: LabVIEW Dataflow
No variables are existing in LabVIEW
  There are data sources and data sinks!
    A priori it is not clear from where data is originating! E.g.:
      From front panel controls in case of interactive mode.
      From calling VI as parameter via connector pane.
  Local and global variables are not really variables with respect to common sense, but different places in memory which are copied by LabVIEW Runtime-Engine asynchronously. This can lead to unintentional race conditions.
Copies of data are created at wire forks.
  The compiler is responsible to maintain a minimum number of copies to be used.
  Therefore LabVIEW is inherent thread-save!
  LabVIEW provides several options to transport data safely with respect to data flow without race conditions between different threads, VIs or loops.
    Queues, Notifications, FGV optionally protected by Semaphore etc.
That’s all true for LabVIEW Objects, too!

## Slide 5: Pros of LVOOP Classes (in comparison to type definitions)
Encapsulation
  Attribute data is always private. It can be changed by class methods only.
  The internal data structure is hidden.
  Access rights: Public, Protected, Private, Community (friend)
Modularity
  Each class has its own clearly defined responsibility.
  The public interface should be well defined.
    It should be modified with very good reason, only!
  Eases testability.
Extensibility
  Derived classes extend the attributes and methods of their ancestor class.
Specialization
  Derived classes special the behavior of their ancestor class.
LabVIEW Objects behave exactly like other LabVIEW data types
  They are following the dataflow paradigm!

## Slide 6: LVOOP Cons and Solutions
There are no real cons.
(Copy-) Constructors and Destructors are not existing.
  They are simply not necessary.
  LabVIEW Objects behave the same as other LabVIEW data types.
Attributes are always private.
  They cannot be displayed or changed directly on the front panel.
  XControls are the solution for this problem.
    XControls can also be used as probes.
Polymorphic class-VIs are not supported.
  Parameters could be implemented as derived class of a common ancestor class.
  Parameters as Variant.
    Especially Variant-Attributes.
Multiple inheritance is not supported.
  An alternative is the Composition design pattern
References to Objects
  Dataflow: Single Element Sized Queue
  Data Value Reference
    Danger of deadlocks

## Slide 7: LVOOP Application
Possible cases for the application of LVOOP classes:
Cluster or type definitions, which become potentially extended, can be replaced with classes.
  Derives classes add attributes to the ancestor class.
Replacement of data type dependent (e.g. Enumeration) Case-Structures by dynamic dispatching.
  Dependent of the objects class the correct corresponding Overwrite-VI is called.
  Beispiel: Queued State-Maschine
Development of generic frameworks
  The application layer uses base classes only.
  Details are implemented in derived classes.

## Slide 8: NI Actor Framework Communication Scheme
Launching Actors
  Actors are derived classes of Actor.lvclass
  Caller-Enqueuer is used by Actor to send messages to the Caller.
  Actor-Enqueuer is used by Caller to send messages to the Actor.
Asynchronous Communication via Queue
  Messages are derived classes of Message.lvclass
  Messages are calling public VIs of an Actor.
  Actor-Messages can be generated automatically be using Tools>Actor Framework Message Maker.

## Slide 9: Example: UPN Calculator
Usage
Stack
Type number
Execute operation
Press enter
Operation executable?
no
yes

## Slide 10: Exercise
Follow the instruction in the course manual to:
  create a project from the Actor Framework-Template
  start the application to test the successful generation
  evaluate the template
  create a class Stack
  modify a template actor to become a UPNCalculator
    test and use it
  modify the other template actor to become a UPNCalculatorGUI

## Slide 11: Referenzen
LabVIEW Menu -> Help -> Search the LabVIEW Help... -> Contents -> Fundamentals -> LabVIEW Object-Oriented Programming
LabVIEW Menu -> Help -> Find Examples -> Browse by Task -> Fundamentals -> Object-Oriented
LabVIEW Object-Oriented Programming: The Decisions Behind the Design
LabVIEW Object-Oriented Programming FAQ
Applying Common OO Design Patterns to LabVIEW
Actor Framework
Measurement Abstraction and Model-View-Controller (MVC) Project with Actor Framework in LabVIEW
HGF Baseclass Library
Mobile Agent System
Thanks to Stephen Mercer for his contributions to web documents & discussions